## Slide 1: Data Transfer And Manipulation
Presented By: Siddhartha Shakya

## Slide 2: Table of contents
Introduction to data transfer instructions.
Different types of data transfer instructions.
Introduction to data manipulation instructions.
Different types of data manipulation instructions.

## Slide 3: Introduction to Data Transfer Instructions
Data transfer simply means moving data from one place to another.
And the instructions that help us transfer data from one place to another without changing the actual content are known as data transfer instructions.
They are also called copy instructions.
Typically the transfers are between:
  memory and processor registers,
  Registers themselves,
  processor registers and I/O devices,

## Slide 4: Typical Data Transfer Instructions
Name | Mnemonic | Definition
Load | LD | Transfer from memory to register (accumulator)
Store | ST | Transfer from register (accumulator) to memory
Move | MOV | Transfer from source to destination
Exchange | XCH | Exchange contents of two registers or register and memory
Input | IN | Transfer from input device to memory
Output | OUT | Transfer from memory to output device
Push/Pop | PUSH/POP | Transfer data between registers and memory stack

## Slide 5: Some Examples of Data Transfer Instructions
Mov
2. LD
Instruction | Result
Mov R1, R2 | Copies the content of R2 to R1
Mov R1, 500 | Immediately put data 500 in R1
Instruction | Result
LD R1 | Copies the content R1 to AC
LD (R1) | Copies the content of memory location whose address is stored in R1 into AC

## Slide 6: Data Transfer Instructions with different addressing modes
Mode | Assembly Convention | Register Transfer
Direct Address | LD ADR | AC <- M[ADR]
Indirect Address | LD @ADR | AC <- M[M[ADR]]
Relative Address | LD $ADR | AC <- M[PC + ADR]
Immediate operand | LD #NBR | AC <- NBR
Index addressing | LD ADR(X) | AC <- M[ADR + XR]
Register | LD R1 | AC <- R1
Register indirect | LD (R1) | AC <- M[R1]
Auto increment | LD (R1)+ | AC <- M[R1], R1 <- R1+1
Auto decrement | LD (R1)- | R1 <- R1 – 1, AC <- M[R1]

## Slide 7: Introduction to Data Manipulation Instructions
Data manipulation refers to processes that transform and operate on data to achieve desired outcomes.
The instructions that help us manipulate data are known as data manipulation instructions.
There are three basic types of data manipulation instructions. They are:
  Arithmetic Instructions,
  Logical and bit manipulation instructions,
  Shift Instructions

## Slide 8: Arithmetic Instructions
Name | Mnemonic | Example | Explanation
Increment | INC | INC R1 | R1 <- R1 + 1
Decrement | DEC | DEC R1 | R1 <- R1 - 1
Add | ADD | ADD R1, R2 | R1 <- R1 + R2
Subtract | SUB | SUB R1, R2 | R1 <- R1 - R2
Multiply | MUL | MUL R1, R2 | R1 <- R1 * R2
Divide | DIV | DIV R1, R2 | R1 <- R1 / R2
Add with carry | ADDC | ADDC R1, R2 | R1 <- R1 + R2 + cy
Subtract with Borrow | SUBB | SUBB R1, R2 | R1 <- R1 – R2 - b

## Slide 9: Logical and Bit Manipulation Instructions
Name | Mnemonic | Example | Explanation
Clear | CLR | CLR R1 | R1 <- 0
Complement | COM | COM R1 | R1 <- R1'
AND | AND | AND R1, R2 | R1 <- R1 AND R2
OR | OR | OR R1, R2 | R1 <- R1 OR R2
Exclusive-OR | XOR | XOR R1, R2 | R1 <- R1 XOR R2
Clear carry | CLRC | CLRC | cy <- 0
Set carry | SETC | SETC | cy <- 1
Complement carry | COMC | COMC | cy <- cy'
Enable interrupt | EL | EL | Enables interrupt

## Slide 10: Shift Instructions
Name | Mnemonic | Explanation
Logical shift right | SHR | Shifts to the right and fills MSB with 0. (Result = x/2)
Logical shift left | SHL | Shifts to the left and fills the LSB with 0. (Result = 2x)
Arithmetic shift right | SHRA | Shifts to the right, preserving the sign. (Copies MSB into the vacated place) (Result = x/2)
Arithmetic shift left | SHLA | Shifts to the left. Sign doesn't change if MSB remains same. (Result = 2x)
Rotate right | ROR | Rotate all bits to the right, with LSB moved to MSB
Rotate left | ROL | Rotate all bits to the left, with MSB moved to LSB
Rotate right through carry | RORC | Similar to ROR but LSB goes to carry flag and the carry flag goes to MSB
Rotate left through carry | ROLC | Similar to ROL but MSB goes to carry flag and the carry flag goes to LSB

## Slide 11: Some Examples of Shift Instructions
SHR (Logical shift right): Result = x/2
2. ROLC (Rotate left through carry)
Instruction | Result
Mov R1, 8CH | R1 <- 10001100 (binary)
SHR R1, 1 | R1 <- 01000110 (46H)
Instruction | Result
MOV R1, 81H | R1 <- 10000001 (binary)
STC 1 | Cy = 1
ROLC R1, 1 | R1 <- 00000011, cy = 1

## Slide 12: Conclusion
In conclusion, data transfer and manipulation is an integral part of a computer system. They help us store, move, exchange and transform the data, through which we can achieve the desired outcomes.

## Slide 13: Thank you!!
ANY QUERIES?